## Slide 1: RAIL/ROAD INTERFACE
TRACK SECTION 1
General Controller (PC)
Serial Bus
24V
POWER SUPPLY 24V CC
Block control interface
CAN BUS
24V
General Controller (PC)
Amplification and channel output + presence detection
PIC18F
S1
S2
Serial Bus
CAN BUS
POWER SUPPLY 24V CC
POWER SUPPLY 24V CC
POWER SUPPLY 20V CC
TRACK SECTION i
Block control interface
TRACK SECTION N
Block control interface
CAN BUS
24V
Master
Slave
Slave
CAN BUS
24V

## Slide 2: PIN ASSIGNMENT
PIC18F4585
PIN | SIGNAL NAME | SIGNAL USED | SCHEMATIC | DIR | FONCTION
1 | MCLR/Vpp/RE3 | MCLR/Vpp | MCLR/Vpp | IN | PIC programming via PICkit2
2 | RA0/AN0/Cvref | AN0 | CURT0 | IN | Track voltage measurement 0
3 | RA1/AN1 | AN1 | CURT1 | IN | Track voltage measurement1
4 | RA2/AN2/Vref- | AN2 | CURT2 | IN | Track voltage measurement2
5 | RA3/AN3/Vref+ | AN3 | CURT3 | IN | Track voltage measurement
6 | RA4/T0CKI | RA4 | S1T0 | OUT | S1 Track 0
7 | RA5/AN4/SS/HLVDIN | AN4 | I/O_4 | IN | KNOB 0 analog value
8 | RE0/RD/AN5 | AN5 | I/O_5 | IN | KNOB 1 analog value
9 | RE1/WR/AN6/C1OUT | RE1 | I/O_6 | OUT | TM1637 SCK I2C bus (mode)
10 | RE2/CS/AN7/C2OUT | RE2 | I/O_7 | OUT | TM1637 SDA I2C bus (mode)
11 | Vdd | Vdd | VCC_5V | IN | +5V
12 | Vss | Vss | GND | IN | GND
13 | OSC1/CLKI/RA7 | RA7 | S2T0 | OUT | S2 Track 0
14 | OSC2/CLK0/RA6 | RA6 | S1T1 | OUT | S1 Track 1
15 | RC0/T1OSO/T13CKI | RC0 | S2T1 | OUT | S2 Track 1
16 | RC1/T1OSI | RC1 | S1T2 | OUT | S1 Track 2
17 | RC2/CCP1 | RC2 | S2T2 | OUT | S2 Track 2
18 | RC3/SCK/SCL | RC3 | S1T3 | OUT | S1 Track 3
19 | RD0/PSP0/C1IN+ | RD0 | S2T3 | OUT | S2 Track 3
20 | RD1/PSP1/C1IN- | RD1 | I/O_0 | IN | Global Purpose Input 0

## Slide 3
PIN | SIGNAL NAME | SIGNAL USED | SCHEMATIC | DIR | FONCTION
21 | RD2/PSP2/C2IN+ | RD2 | I/O_1 | IN | Global Purpose Input 1
22 | RD3/PSP3/C2IN- | RD3 | I/O_2 | IN | Global Purpose Input 2
23 | RC4/SDI/SDA | RC4 | I/O_3 | IN | Global Purpose Input 3
24 | RC5/SDO | RC5 | IDENTBIT2 | IN | BIT 2 card identifier
25 | RC6/TX/CK | RC6 | IDENTBIT3 | IN | BIT 3 card identifier or TX line if MAX232 installed
26 | RC7/RX/DT | RC7 | IDENTBIT4 | IN | BIT 4 card identifier or RX line if MAX232 installed
27 | RD4/PSP4/ECCP1/P1A | RD4 | IDENTBIT1 | IN | BIT 1 card identifier
28 | RD5/PSP5/P1B | RD5 | IDENTBIT0 | IN | BIT 0 card identifier
29 | RD6/PSP6/P1C | RD6 | OUT0 | OUT | Low-power control (points, low beam, lighting, level crossings, various motors)
30 | RD7/PSP7/P1D | RD7 | OUT1 | OUT | Low-power control (points, low beam, lighting, level crossings, various motors)
31 | Vss | Vss | VCC_5V | IN | +5V
32 | Vdd | Vdd | GND | IN | GND
33 | RB0/INT0/FLT0/AN10 | RB0 | OUT2 | OUT | Low-power control (points, low beam, lighting, level crossings, various motors)
34 | RB1/INT1/AN8 | RB1 | OUT3 | OUT | Low-power control (points, low beam, lighting, level crossings, various motors)
35 | RB2/INT2/CANTX | CANTX | CANTX | IN/OUT | Bus CAN Transmission
36 | RB3/CANRX | CANRX | CANRX | IN/OUT | Bus CAN Reception
37 | RB4/KBI0/AN9 | RB4 | OUT4 | OUT | Low-power control (points, low beam, lighting, level crossings, various motors)
38 | RB5/KBI1/PGM | RB5 | OUT5 | OUT | Low-power control (points, low beam, lighting, level crossings, various motors)
39 | RB6/KBI2/PGC | PGC | PGC | IN/OUT | PIC programming via PICkit2
40 | RB7/KBI3/PGD | PGD | PGD | IN/OUT | PIC programming via PICkit2

## Slide 4: Channel signal amplification

## Slide 5: Communication via CAN bus
Remember the termination resistor on the last element!